## Slide 1
AeroSpace and Defence
Industries Association of Europe
Jean-Yves DELAUNAY: Airbus
AIA - ASD interoperability coordination confcal
25th of April 2018
: Business opportunity for process planning information interoperability based on ISO open standard

## Slide 2: Context
Strong effort to ensure the end to end digital continuity / interoperability of the Model Based Engineering  Model Based manufacturing
Interoperability of Process Plan information becomes critical for seamless communication for the Production Planning and for the Final Assembly Lines
Identification of draft use cases for Process Plan information interoperability:
    3D MB definition and 3D MB manufacturing for Holes and Fasteners (including the operations in the shop floor)
    Communication of 3D Working Instruction Sheets / 3D Manufacturing process plans between heterogenous systems
        Manufacturing Engineering (preparation) => Manufacturing Execution Systems
    Consistency between macro process planning and micro process planning (part manufacturing, such as AP238)

## Slide 3
Process plan capability, part of ISO STEP AP242 edition 1 (IS 2014)

## Slide 4
Overview of the AP242 ed1 “Business Object Model”
SEE Next page
Click on the icon

## Slide 5
This capability enables the representation of process related data.
This includes process plans, versions of process plans with version tracking, process operations and properties of processes.
A process plan is decomposed into one or more occurrences of process operations.
Process plans and process operations establish relationships among raw materials, in-process items, and final items, as well as the relationship between the items and the tools used to manufacture them.
Additionally, the representation of the connection of parts in various kinds of mating is part of this capability.
AP242 “Process Plan” capability

## Slide 6
Overview of the STEP AP242 ed1 : objects and relationships of the “Process Plan”
capability
Process Operation Occurence
Process Plan
Process Plan Relationship
Process Operation Resource Assignment
Process
Operation
InputOrOutput
ProcessOperation Definition Relationship
Process Operation Definition
Process Operation Occurrence Relationship
On the AP242 HTML documentation
: To click on the object To have access to its textual definition

## Slide 7
plan
assignedTo
operation
Process Operation Occurence
Process Plan
Process Operation Resource Assignment
Process
Operation
InputOrOutput
Process Operation Definition
Overview of STEP AP242 ed1 objects and relationships of the “Process Plan” capability
Definition
A ProcessPlan is manufacturing planning information, necessary to realize or produce a particular version of a Part.
A ProcessOperationOccurrence is a usage of a ProcessOperationDefinition in a ProcessPlan.
This association states that the ProcessOperationDefinition is part of the ProcessPlan.
A ProcessOperationInputOrOutput is an input or expected result of a ProcessOperationDefinition
A ProcessOperationDefinition is a specification of an activity that may be included in a ProcessPlan.
A ProcessOperationDefinition characterizes a manufacturing or control operation. .
A ProcessOperationResourceAssignment is a mechanism to associate a resource with a ProcessOperationOccurrence.
Example: a tool
Example: Aircraft sub assembly
'stamping', 'milling', 'drilling', 'welding', 'casting', and 'painting' are examples for processType

## Slide 8: ISO 10303 AP 240 Figure 1: Process planning data planning model

## Slide 9: STEP AP 242 « Process plans for machined products » A-0 Process plans for machined parts

## Slide 10: Interoperability architecture framework for Process Planning information
STEP AP242
Managed model based 3D engineering
STEP AP240
Process plans for machined products
STEP AP238 ed2
Model based integrated manufacturing
Business
requirements
Processes & Use cases
Information models & implementation formats
PLM
Applications
Interoperability test rounds
Process Plan IF
xDM IF
To be completed
3D MB Manufacturing IF
CAx IF

## Slide 11: Summary – next actions
To confirm the interest of the American and European A&D industries to define joined recommendations for interoperability of process plan information
To agree on the related ISO information model standards, such as:
    AP242 ed1
To continue to identify the main interdependancies based on the Interoperability architecture framework (4 layers)
    Industry 4.0
To define use cases for process plan interoperability and associated public test cases