## Slide 1: Strategic Standardisation Group Standards Radar Chart
V1.10 – Revision d, 3/10/2019
Copyright © 2019 AeroSpace and Defence Industries Association of Europe - ASD
(based upon AIA presentation principle)

## Slide 2: Executive Summary
The SSG Radar Chart shows the various technology standards under the attention of the SSG.
The Adopt Existing Standard quadrant refers to standards which have been developed outside of ASD but which have relevance to the ASD.
The Monitor External Development quadrant refers to standards which are being developed outside of the ASD but which may have relevance to the ASD.
The Participate in External Development quadrant refers to outside standards development where SSG members are actively participating and influencing.
The ASD Development quadrant shows standards and templates that the SSG is developing internally
Through this synthesis view, the SSG intends to build on the methods developed by AIA and to develop a common Aerospace view on e-Business Standards.

## Slide 3: Process Overview
Standards begin in the outer “Track” ring while the SSG reviews and/or evaluates the standard.
If a standard demonstrates relevance to ASD needs, it is promoted to the “Candidate” ring for deeper review.
Candidate Standards that the SSG deems stable and relevant are presented to the ASD SSG Members for adoption as an ASD standard. It is recommended that candidate standards are proven through pilot implementations prior to adoption.
Candidates adopted by the ASD SSG Members are promoted to the inner “Adopted” ring and enter a review and maintenance cycle.

## Slide 4: Criteria for adoption
Criteria for a standard to be “Adopted”:
  Standard officially published and available
  Consistency of the standard with the ASD Through Life-cycle interoperability policy
    Refer to the related report on ASD SSG website, at www.asd-ssg.org/through-life-cycle-interoperability
  Adoption statement validated by ASD members (the adoption statement could refer to any pilot implementations/deployments)

## Slide 5
Radar screen
Monitor
external
development
Participate in
external
development
Available
external
standards
ASD
development
Version: V1.10d (October 2019)
yy
Blip available
Blip in preparation
yy
Current ASD SSG actions
d
Supplier
UID
PLCS
DEXs
OAGIS
ISO 8000
RFID
App Stds
STEP
SysML
STEP AP233
XPDL
STEP AP212
STEP AP235
STEP AP210
EN9300 LOTAR
SAML
ISO 22745
VEC KBL
S1000D
ebXML
3D Visualisation
BPMN
STE100
S5000F
TDP message
STEP AP242ed1
Boost Aero
S4000P
S2000M
STEP AP214
STEP AP203
S3000L
STEP AP239ed2
TSCP SEv1
EN9300-2xx
SCORM
EN9300-3xx
EN9300-4xx
ISO 12306
JT V2
PRC/U3D
COLLADA
SX000i
EN9300-1xx
Modelica
FMI
VDA4969
PAS55
STEP AP209
MIMOSA
IEEE 1636
S6000T
SX001G
SX002D
EN9300-6xx
OSLC
ArchiMate
UAF
GEIA-0007
MoSSEC
STEP AP242ed2
Track
Candidate
Adopted
STEP AP238
ReqIF
QIF
SPEC2000
SPEC2300
iSPEC2200
SPEC42
SPEC1000BR
STEP AP239ed3
STEP
ASD S-Series
3D visualisation
LOTAR
ATA eBusiness
EN9300-5xx

## Slide 6: 3D Visualisation
Abstract
The design and manufacture of today’s products is largely based on 3D electronic models developed on CAx systems. While these tools provide powerful capabilities for developing product definitions, the objective of 3D visualization is to allow the resulting information to be viewed across a wider population without the need for high-end CAD workstations or CAD software licences. This facilitates review and information use, accelerating product development. Standard information formats for visualization allow such tools to be used to view information generated by different native CAx systems.
Visualization is not intended to replace or overlap CAx systems functionalities. It is not intended to replace existing CAx data exchanges but to complement it in those cases where the data receiver does not need the functionality of the authoring system and only requires a selected subset of the completed information model. In addition, a sender, in order to protect intellectual property, may not wish to release underlying constructional information and the knowledge included in a rich CAx data model, but may wish to disclose only selected information. Visualisation data is destined for a data consumer rather than for a data creator or updater.
Click the icon below
to view the details.
Last revised: 2010-04-02
Back to the Radar
Notes: 6

## Slide 7: ArchiMate
Abstract
ArchiMate is an open and independent enterprise architecture modeling language to support the description, analysis and visualization of architecture within and across business domains in an unambiguous way.
ArchiMate is a technical standard from The Open Group and is based on the concepts of the IEEE 1471 standard. It is supported by various tool vendors and consulting firms.
ArchiMate distinguishes itself from other languages such as Unified Modeling Language (UML) and Business Process Modeling Notation (BPMN) by its enterprise modeling scope.
Last revised: 2014-08-18
Back to the Radar
Click the icon below
to view the details.

## Slide 8: BoostAero
Abstract
The BoostAero initiative was initially established as a joint French and Exostar initiative to achieve a standardized set of procurement e-trading messages, in order to avoid a proliferation of incompatible portals. This deliberately sought to build on the internationally agreed set of core components for ebXML by working through UN/CEFACT, in order to ensure interoperability with other electronic trading environments. The initial set of messages has been developed and piloted, and is now being deployed in production use.
It was recognized at an early stage that the diversity of the global aerospace supply chain meant that the business objective could only be achieved by seeking global adoption of the standard. The BoostAero team therefore approached European ASD and American AIA seeking broader acceptance of their approach. The initial AIA due diligence process highlighted no major obstacles to use of BoostAero, but some need for modifications, similar to the European view.
The BoostAero standard has been adopted in 2009 by the BoostAeroSpace Hub founders (i.e. Airbus, Dassault-Aviation, EADS, Safran, Thales) as the standard for exchanges on AirSupply between customers and suppliers. This will generalize the use of BoostAero standards in the A&D Supply Chain.
Last revised: 2016-09-13
Back to the Radar
Click the icon below
to view the details.

## Slide 9: BPMN - Business Process Modelling Notation
Abstract
BPMN is a standardized graphical notation that depicts the steps in a business process and the end-to-end flow of a business process.
It has been specifically designed to coordinate the sequence of processes and the messages that flow between different process participants in a related set of activities. It targets at facilitating communication between users, business analysts, vendors and service providers that need to communicate business process in as standardized manners, within eBusiness context.
Last revised: 2011-11-14
Back to the Radar
Click the icon below
to view the details.
Notes: 9

## Slide 10: COLLADA - COLLAborative Design Activity
Abstract
The COLLADA format is a file format for exchange between 3D applications (including games). COLLADA file is an XML file. The specification and the XML-based schema are publicly available. Collada 1.5 specification was published in April 2008 by Khronos Group.
Example of applications and software supporting COLLADA: 3dsMax, 3Dvia, Blender, Photoshop.
The features supported are:
  B-rep geometry / Mesh geometry / Level of Detail and Streaming
  Instantiation
  Transform hierarchy (rotation, translation, shear, scale, matrix)
  Compressed Exchange format
  Animation / Kinematics
  Physics (rigid bodies, constraints, rag dolls, collision, volumes)
  Shaders / Materials/ Textures / Lights /Skinning
  Cameras
ISO/PAS 17506:2012 Industrial automation systems and integration -- COLLADA digital asset schema specification for 3D visualization of industrial data was published in July 2012.
Last revised: 2014-08-19
Back to the Radar
Click the icon below
to view the details.
Notes: 10

## Slide 11: ebXML Core Components
Abstract
The ebXML Core Components Technical Specification can be employed wherever business information is being shared or exchanged amongst and between enterprises, governmental agencies, and/or other organizations in an open and worldwide environment. The Core Components provides business people, business document modelers and business data modelers, Business Process modelers, and application developers of different organizations a common set of vocabulary building blocks to support interoperability of business information. This interoperability covers both interactive and batch exchanges of business data between applications through the use of Internet and Web based information exchanges as well as traditional Electronic Data Interchange (EDI) systems.
The ebXML Core Components Technical Specification, Version 2.01 (ebCCTS) is also published as ISO/TS 15000-5. Under the governance of UN/CEFACT TBG17, a library of approved core components is available for various standards organizations to use as building blocks for their transactions.
These core components provide the basis for the XML-based, eBusiness vocabularies to be used for our global Aerospace & Defense industry. The core components are the foundation for the evolving BoostAero set of aerospace ebusiness transactions.
Last revised: 2010-04-29
Back to the Radar
Click the icon below
to view the details.

## Slide 12: FMI - Functional Mock-up Interface
Abstract
Functional Mock-up Interface (FMI) is a tool independent standard to support both model exchange and co-simulation of dynamic models using a combination of xml-files and compiled C-code. FMI improves and simplifies the exchange of dynamic system models between different modelling, simulation and co-simulation tools. Applications range from software/model/hardware-in-the-loop simulation to embedded systems.
Initially developed in the European (ITEA2) MODELISAR R&D project, FMI has been managed and developed since 2011 as a Modelica Association Project (MAP).
In the FMI approach, models are packaged in Functional Mock-up Units (FMUs, with a given zip file structure) and can then be integrated in another simulation environment (model integration) or coupled at runtime in a distributed simulation (co-simulation).
FMI 2.0, published in July 2014, provides significant enhancements compared to FM1 1.0, both for model exchange and for co-simulation. Moreover in FMI 2.0 a significant effort has been done to merge the two FMI 1.0 standards (Model Exchange and Co-Simulation) in one consistent standard.
Last revised: 2018-11-12
Back to the Radar
Click the icon below
to view the details.

## Slide 13: ISO 14306 - JT Edition 2
Abstract
ISO 14306 provides the description of the structure and content for a binary file having the extension of .jt. A binary file with the .jt extension is generally referred to as a JT file. The ISO 14306 format is used primarily in industrial use cases as the means for capturing and repurposing lightweight 3D product definition data.
The JT format is an industry focused, high-performance, lightweight, flexible file format for capturing and repurposing three-dimensional product definition data that enables collaboration, validation and visualization throughout the extended enterprise.
ISO 14306:2017 defines the syntax and semantics of a file format for the 3D visualization and interrogation of lightweight geometry and product manufacturing information derived from CAD systems, using visualization software tools that do not need the full capability of a CAD system.
This document has been adopted as a 3D visualization capability in addition to the ISO 10303 series.
Last revised: 2019-04-23
Back to the Radar
Click the icon below
to view the details.

## Slide 14: ISO 22745 Open technical Dictionaries and automated data exchange
Abstract
The initiative is intended to enshrine the practice and capability of Electronic Open Technical Dictionaries and used to support automated data transactions between participating entities.
It provides a common structure for defining open technical dictionaries as repositories of sets of terminology derived from other standards, with links back to the originating document. Such repositories can accommodate multiple definitions of the same term, although each definition will have its own unique identification
The dictionaries can then be used to set up catalogues and classification schemes using the terminology in the dictionaries to define property-values pairs, with terms resolvable over the Internet using the unique identifiers.
A further application of the dictionaries links the properties of features in STEP product definitions to the NATO Codification Scheme, and also to automatically generate STEP product definitions from the characteristic properties.
This standard in conjunction with ISO 8000 Pt 110 has been used in trials to generate automatically from source technical descriptions in accordance with the US Federal Item Identification Guides and NATO Codification System. The trials used a schema provided by ECCMA as part of the only currently accredited ISO 22745 OTD (ECCMA Open technical Dictionary)
Last revised: 2011-11-28
Back to the Radar
Click the icon below
to view the details.

## Slide 15: ISO 8000 - Data Quality
Abstract
The ISO 8000 series of standards covers data quality activities, terminology, characteristics (criteria) and testing. Data quality is a pervasive problem for organizations across the globe and has a major economic impact. No one nation can afford to develop a unique perspective on the solution to this problem. The standard is applicable to all types of industrial data, including master data, transaction data and product data.
ISO 8000 defines characteristics that can be tested by any organization in the data supply chain to objectively determine conformance of the data to ISO 8000. ISO 8000 does not require external certification of data quality. Therefore, data quality conformance can be self-controlled.
ISO 8000 provides a framework for improving data quality that can be used independently or in conjunction with quality management systems.
Last revised: 2012-03-14
Back to the Radar
Click the icon below
to view the details.

## Slide 16: EN9300 LOTAR - Long Term Archiving and Retention
Abstract
The LOTAR project is designed to provide a capability to preserve digital aerospace and defence product information in a standard neutral form that can be read and reused throughout its lifecycle, independent of changes in the IT application environment originally used to create it.
The multi-part standard covers the requirements, the information content and the processes required to ingest, store, administer, manage and access the information.
The LOTAR international project brings together the works started in Europe by ASD Stan LOTAR, supported by ProSTEP iViP, and the US similar works started by PDES Inc and AIA, under the auspices of the International Aerospace Quality Group (IAQG).
This general recommendation of the ASD SSG regarding the LOTAR standards are completed by other SSG recommendations per specific domains:
  LOTAR 3D PMI : long term preservation of 3D PMI information,
  LOTAR PDM : long term preservation of PDM information.
  LOTAR Composite : long term preservation of Composite information.
  LOTAR Electrical : long term preservation of Electrical Harness information,
Last revised: 2012-10-05
Back to the Radar
Click the icon below
to view the details.

## Slide 17: EN9300-1XX - Long-Term Archiving and Retrieval of 3D Geometry, CAD structure and Product Manufacturing Information (LOTAR 3D CAD)
Abstract
The LOTAR The LOTAR project is designed to provide a capability to preserve digital aerospace and defence product information in a standard neutral form that can be read and reused throughout its lifecycle, independent of changes in the IT application environment originally used to create it.
This document focuses on the EN9300-1XX family for long term archiving and retrieval of CAD mechanical information, including assembly structure, 3D Geometric shape representation (explicit and implicit), associated Product and Manufacturing Information (PMI), and machining form features.
The EN9300-1XX family is organized as a sequence of parts, each building on the previous in a consistent way. Some of the EN9300-1XX standards are adopted and exploited by the Aerospace and Defence industry. As technology matures additional parts will be released in order to support new requirements within the aerospace community.
Last revised: 2012-10-05
Back to the Radar
Click the icon below
to view the details.

## Slide 18: EN9300-2XX - Long-Term Archiving and Retrieval of Product Management Data & Configured Mechanical Product Structure (LOTAR PDM)
Abstract
The LOTAR project is designed to provide a capability to preserve digital aerospace and defense product information in a standard neutral form that can be read and reused throughout its lifecycle, independent of changes in the IT application environment originally used to create it.
This document focuses on the ASD EN9300-2XX family for long term preservation of the Product Management Data Information throughout lifecycle.
The EN9300-2XX family is organized as a sequence of parts, each building on the previous in a consistent way. Some of the EN9300-2XX standards are draft. As technology matures additional parts will be released in order to support new requirements within the aerospace community.
Last revised: 2012-10-05
Back to the Radar
Click the icon below
to view the details.

## Slide 19: EN9300-3XX - Long-Term Archiving and Retrieval of Composite Information (LOTAR Composite)
Abstract
The LOTAR The LOTAR project is designed to provide a capability to preserve digital aerospace and defence product information in a standard neutral form that can be read and reused throughout its lifecycle, independent of changes in the IT application environment originally used to create it.
This document is focused on the EN9300-3XX family for the long term archiving and retrieval of the composite structures.
The EN9300-3XX family is organized as a sequence of parts, each building on the previous in a consistent way. EN9300-3XX standards are in development and will be adopted and exploited by the Aerospace and Defense industry. As technology matures additional parts will be released in order to support new requirements within the aerospace community.
Last revised: 2012-10-05
Back to the Radar
Click the icon below
to view the details.

## Slide 20: EN9300-4XX - Long-Term Archiving and Retrieval of Electrical Harness Information (LOTAR Electrical Harness)
Abstract
The LOTAR project is designed to provide a capability to preserve digital aerospace and defence product information in a standard neutral form that can be read and reused throughout its lifecycle, independent of changes in the IT application environment originally used to create it.
This document is focused on the EN9300-4XX family for the long term archiving and retrieval of Electrical Harness information.
The EN9300-4XX family is organized as a sequence of parts, each building on the previous in a consistent way. Some of the EN9300-4XX standards are adopted and exploited by the Aerospace and Defense industry. As technology matures additional parts will be released in order to support new requirements within the aerospace community.
Last revised: 2012-10-05
Back to the Radar
Click the icon below
to view the details.

## Slide 21: EN9300-5XX - Long-Term Archiving and Retrieval of Model-based Systems Engineering Information (LOTAR MBSE)
Abstract
The purpose of the Model Based Systems Engineering Workgroup (MBSE WG), launched in April 2018, is to define a set of LOTAR standards, shared by international aerospace and defence industries, for the long term preservation of Model Based Systems Engineering (MBSE) Information, taking into account the consistency with the other relevant LOTAR parts. Although these standards may apply to other industries, the definition is a critical part of the type design of aerospace and defence systems and is subject to the same long term retention requirements as other parts and features.
The objective of the workgroup is to develop, publish and maintain standards-based mechanisms for archiving and retrieval of Model Based Systems Engineering information that can be read and reused throughout the product lifecycle, independent of changes in the Information Technology (IT) application environment originally used for creation. The focus is on the long term preservation of the MBSE inputs, results and metadata for the design, manufacturing and support of aerospace products.
Last revised: 2019-10-03
Back to the Radar
Click the icon below
to view the details.

## Slide 22: MIMOSA Machinery Information Management Open Systems Alliance
Abstract
MIMOSA is a not-for-profit trade association dedicated to developing and encouraging the adoption of open information standards in operations and maintenance (O&M) in manufacturing, fleet, and facility environments.
MIMOSA has developed two information-exchange open standards, providing for example metadata reference libraries and a series of information-exchange standards using XML and SQL:
  A standard for management applications: Open Systems Architecture for Enterprise Application Integration (OSA-EAI™)
    Includes modelling, metadata, source, query/response, historicity, etc.
    Applicability: Diagnostics, prognostics, trending, test, and maintenance, Acquisition of built-in-test results, storage of raw and transformed data, and exchange of data for analysis and viewing
  A standard for condition-based maintenance: Open Systems Architecture for Conditioned Based Maintenance (OSA-CBM™)
    Object interfaces (modules with exposed methods)
    Platform oriented (helicopter, vehicle, ship).
Last revised: 2014-08-25
Back to the Radar
Click the icon below
to view the details.

## Slide 23: Modelica
Abstract
Modelica® is a non-proprietary, object-oriented, declarative, equation based language to conveniently model complex physical systems containing, e.g., mechanical, electrical, electronic, hydraulic, thermal, control, electric power or process-oriented subcomponents..
Modelica is a free language developed by the (non-profit) Modelica Association since 1996. The Modelica Association develops also the a free library for multi-domain models: the Modelica Standard Library.
The Modelica design effort was initiated in September 1996. The goal was to develop an object-oriented language for modeling of technical systems in order to reuse and exchange dynamic system models in a standardized format. Modelica supports behaviours described by differential, algebraic, and discrete equations, enabling a large spectrum of 0D/1D simulations. 3D simulation based on partial differential equations (e.g. FEM, CFD) is not supported, but results of such simulations can be integrated (e.g. using surrogate models).
Last revised: 2013-09-09
Back to the Radar
Click the icon below
to view the details.

## Slide 24: MoSSEC - Modelling and Simulation in Collaborative Systems Engineering Context
Abstract
The ISO MoSSEC project (ISO 22071) is designed to provide a capability to share modelling and simulation (M&S) information in a collaborative systems engineering context, and to enable full traceability and re-use of this information throughout the product lifecycle and independent of the specific IT applications used across collaborating enterprises.
The targeted standard covers a core subset of systems engineering information content and the related practices and information services necessary to support engineering collaboration.
The ISO MoSSEC international project brings together the works started in Europe by CRESCENDO and TOICA Consortia to apply AP233/AP239 for this scope, and similar works in Europe and US motivated by similar goals.
The project deliverable will be a new STEP Application Protocol [AP] under ISO TC 184/SC 4 within the New STEP Architecture and utilising a subset of the AP239/AP242 harmonised information model. This AP (provisionally entitled AP243) will include an activity model for usage guidance; AP-level definitions for agreed implementation technologies; conformance classes; documentation and dissemination material.
Last revised: 2019-01-31
Back to the Radar
Click the icon below
to view the details.

## Slide 25: OAGIS Open Applications Group Integration Specification
Abstract
The specification provides a set of standardized XML messages for use throughout the supply chain. It defines a series of Business Object Definitions (BODs) to support the standardized exchange of typical messages used in B2B applications for commercial supply chain and accounting transactions.
Each BOD comprises a Verb (get, show, list, process etc.) and a Noun (purchase order, shipping list, invoice, BoM etc.). Some 16 verbs and 75 nouns are defined by OAGIS 9. Messages can be tailored to meet local user requirements. Brief scenarios are provided to illustrate usage of most BODs.
EDS used selected nouns from OAGIS 8 as an integration model for the UK MoD Supply Enterprise Information Architecture (EIA) hub. OAGIS 8 has also been applied to a few messages linking the Log Info System, LITS, to the EIA Hub on the Tornado ATTAC project.
OAGIS 9 differs from the earlier versions due to alignment with the ebXML Core Components Library (see separate blip) developed by OASIS and UN/CEFACT, which is the agreed international approach for transactional messages. There has been a deliberate decision to break upward compatibility to address this alignment.
The specification is freely available for download from the OAGi site
Last revised: 2016-09-13
Back to the Radar
Click the icon below
to view the details.
Notes: 25

## Slide 26: OSLC - Open Services for Lifecycle Collaboration
Abstract
Open Service for Lifecycle Collaboration (OSLC) is an open community, originally proposed in 2008, to define a set of specifications that enable integration of software development and more broadly Application Lifecycle Management (ALM) and Product lifecycle Management (PLM) products and services.
The OSLC initiative is divided up into a dozen workgroups and each workgroup develops specifications in context of a specific part of the lifecycle. For example, there are workgroups for Change Management, Quality Management, Requirements Management, Software Configuration Management and Build Automation.
As of June 2013, the OSLC initiative is a Member Section of the Open Standard Organization OASIS.
The OSLC specifications build on the W3C Resource Description Framework (RDF), Linked Data and REST, enabling integration at data level via links between related resources. OSLC resources are defined in terms of RDF properties. Operations on resources are performed using HTTP. OSLC also specifies user interface techniques to enable preview, creation and selection of links.
Last revised: 2014-18-08
Back to the Radar
Click the icon below
to view the details.
Notes: 26

## Slide 27: PRC/U3D - Open Services for Lifecycle Collaboration
Abstract
The PDF format is a file format for the representation of documents. PDF allows to preserve the layout (text, font, graphics and other information). It is independent of the operating system and the software. PDF was originally developed by Adobe Systems in 1993. The open format has been published by the ISO in 2008.
PDF/E is a subset of pdf. The intent is the exchange of engineering and technical data.
  The part 1 of PDF/E published by the ISO in 2008 include the U3D format.
  The part 2 of PDF/E will include the PRC 1.0 format.
U3D is a file format for 3D data. U3D was originally develop by a group including Intel, Boeing, HP, Adobe Systems. U3D standard has been published in 2006 by ECMA international.
PRC is a file compressed format allows to have different representation of a 3D model. PRC was originally developed by TTF. PRC format has reached the Draft International Standard stage in 2012.
Last revised: 2014-08-19
Back to the Radar
Click the icon below
to view the details.
Notes: 27

## Slide 28: PAS 55:2008 BSI Publically Available Specification Asset Management
Abstract
PAS 55 defines the requirements for an integrated and cohesive Asset Management system, providing a clear “line of sight” from organization direction and goals down to individual, day-to-day activities.
Asset Management in this context is the systematic and coordinated activities and practices through which an organization optimally manages assets and systems, their performance, risks and expenditures over their life cycles for the purpose of achieving the organisational strategic plan.
To ensure consistency with other related management system standards, PAS 55 was documented as a specification, with the information on implementing asset management distilled into key requirements. The criterion for including such requirements has been that, without them, the asset management system would be regarded as deficient.
This Specification is applicable to any organization where physical assets are a critical factor in achieving its goals.
Last revised: 2013-09-09
Back to the Radar
Click the icon below
to view the details.
Notes: 28

## Slide 29: RFID Application Standards
Abstract
Radio Frequency Identification (RFID) provides the capability to attach identity and other information to a physical object in the form of an electronic tag, which can be accessed remotely through a radio frequency reader and transmitted to application software.
RFID tag hardware consists of a computer chip plus antenna which can be read from, and optionally written to, using an RF reader via radio frequency. Tag and Reader can operate in active mode with battery powered tags or in passive mode using reader power.
Basic RFID is used to locate, track and identify assets and commodities, and to trigger events such as information exchange. New RFID capabilities offer a range of business opportunities for attaching additional information to a tagged product or shipping container and exploiting that information to streamline business processes.
RFID applications are now being developed for Transportation, Logistics, Material / Inventory Management and Aircraft Maintenance in the Aerospace and Defense (A&D) Industry.
  ERP and MRP applications supporting RFID applications
  Multiple Industry verticals defining cross industry RFID data vocabularies
Last revised: 2010-03-10
Back to the Radar
Click the icon below
to view the details.

## Slide 30: S1000D - Specification for Technical Publications
Last revised: 2014-08-13
Abstract
The international specification for technical publications using a common source database, commonly known as S1000D, has been produced to establish standards for the technical documentation of any civil or military vehicle or equipment. It is based on international standards such as XML and CGM for production and use of electronic documentation.
In addition, it defines a Common Source Data Base (CSDB) to provide source information for compilation of the publications and for use in electronic logistics information systems to deliver modules of information direct to the user.
S1000D is linked to the PLCS development, which enables the compilation of technical documentation direct from the current product structure. The specification also includes rules and XML Schemas to enable the production of SCORM-compliant Web Based Training (WBT).
Back to the Radar
Click the icon below
to view the details.

## Slide 31: S2000M International specification for material management specification
Last revised: 2011-09-30
Abstract
The ASD S2000M defines the Materiel Management processes and procedures to be used in support of any military Product.
Although this Specification is designed for military Product support, it may nevertheless be used for the support of any non-military Product.
The S2000M describes the business relationship between Industry and Customer by providing the process flow, the relevant transactions and data elements used.
The S2000M is organized into basic chapters:
  Chapter 1A Provisioning
  Chapter 1B NATO Codification
  Chapter 2 Procurement Planning
  Chapter 3 Order Administration
  Chapter 4 Invoicing
  Chapter 5 Repair Administration
  Chapter 6 S2000M Light
Back to the Radar
Click the icon below
to view the details.
Notes: 31

## Slide 32: S3000L - International procedure specification for Logistic Support Analysis LSA
Last revised: 2015-03-31
Abstract
With the introduction of a new and complex technical product, all logistic requirements must be made available in a timely manner. This requires a process to ensure consideration of logistic requirements during the design of the product and support the establishment of a proper support system. The LSA process includes a number of analysis activities concerning a wide range of technical and logistic considerations and the careful documentation of the results of these analysis activities. The achievement of proper supportability is of crucial importance concerning operation and life cycle costs. Early consideration of logistic aspects is increasingly important with regard to both operational and economic aspects. A product that cannot be operated and maintained properly and cost effectively is not acceptable to the end user.
The purpose of the specification S3000L is to cover the activities and requirements governing the establishment of the LSA process.
Back to the Radar
Click the icon below
to view the details.

## Slide 33: S4000P - International specification for developing and continuously improving preventive maintenance
Last revised: 2014-07-08
Abstract
According to the ASD scope, S4000P must cover all kind of Product types including any complex technical platform, system, equipment or facility (eg. on air/sea/land, under sea, under ground, in space).
The main purpose of ASD S4000P is to assist regulatory authorities and all parties involved in the analysis process in developing and releasing initial Preventive Maintenance Task Requirements (PMTR) and intervals for new Products prior entry into service. The S4000P analysis methodologies remain applicable for later optimizations/modifications of the Product design in Product systems and/or of Product structure and/or of Product zones during the Product in-service phase.
Once developed, authorized and packaged into interval clusters in a Product Operator Maintenance Program (OMP), the S4000P In-Service Maintenance Optimization (ISMO) process enables continuous improvement of Product maintenance during the in-service phase.
Every development of a PMTR or later improvements of a preventive maintenance task for a Product is linked to at least one of the following aspects:
  Ensure / maintain Product safety, including safety/emergency systems and/or emergency equipment,
  Avoid any conflict with law and/or significant impact on environmental integrity (ecological damage) during Product mission/operation and/or maintenance,
  Optimize mission/operational capability/availability of the Product,
  Optimize Product economy (Life Cycle Costs = LCC).
Back to the Radar
Click the icon below
to view the details.
Notes: 33

## Slide 34: S5000F - Operational and Maintenance Data Feedback
Last revised: 2017-02-02
Abstract
In-service data feedback is one of the most important functions of in service support. It enables fleet managers, support managers and technical system manufacturers to perform a thorough analysis of operational and maintenance performance of a technical system.
The results of the analysis can be the basis for:
enhancement of the maintenance and support concept
improvement of the product or the system by modifications and retrofit activities
sophisticated operational planning
management of requirements and contracts
The overall aim to be achieved through in-service data feedback is the increase of fleet availability and optimization of effectiveness. In addition the in-service data feedback information is a firm requirement by industry to agree to and manage Performance Based Logistics (PBL) contracts and to fulfil their obligations in the regard to product liability.
The aim with S5000F is to handle information from the in service operation (from the operator to the Product manufacturer or the maintainer) or vice-versa during the in-service phase. The processes used for this are described in the specification, with the focus on specific use cases that are associated to activities that typically require in-service data feedback. The association of data feedback to specific use cases ensures that no unnecessary information is requested from the field.
Back to the Radar
Click the icon below
to view the details.

## Slide 35: S6000T - International specification for Training Analysis and Design
Last revised: 2018-11-30
Abstract
Training and Training Support consists of the processes, procedures, techniques, training devices and equipment used to train personnel to operate and support a system. The development of an effective training solution is critical to ensure the alignment between system design and the overall support of that system.
S6000T is taking a process based architectural approach and detailing the processes steps required to complete these 2 phases, to understand the data inputs and outputs for each of these steps. The S6000T working group is using Department of Defense Handbook 29612, Instructional Systems Development/Systems Approach to Training and Education, as well as several international guidance’s to understand and harmonize the process steps and data requirements.
S6000T is the latest S-series specification being drafted by AIA/ASD with the purpose of standardizing the data delivered by the different supportability elements as well as to standardize the data exchanges between the different support elements.
Back to the Radar
Click the icon below
to view the details.

## Slide 36: SX000i - International guide for the use of the S-Series Integrated Logistics Support (ILS) specifications - (“ILS Guide”)
Abstract
Integrated Logistic Support (ILS) is the integrated management of the definition and development of all support resources, using a common process and methodology, so as to harmonize the different support elements, prevent unnecessary rework and reduce overall life-cycle costs.
The SX000i has been developed to ensure the compatibility and the commonality of ILS processes among the AIA/ASD S-Series ILS specifications. By providing a single framework that documents the global ILS process and interactions, and by defining governance requirements for the S-Series ILS Specifications, the SX000i and S-Series Specifications will enable all stakeholders to apply common logistics processes so as to share and exchange data securely through the life of products and services.
Through the secure and standardized exchange of data and information, product performance and life cycle cost can be more easily analyzed and optimized, and collaboration between customers and industry can be simplified.
Last revised: 2017-02-02
Back to the Radar
Click the icon below
to view the details.

## Slide 37: SX001G - Glossary for the S-series ILS specifications
Last revised: 2015-02-10
Abstract
With the drive for an integrated set of Integrated Logistic Support (ILS) specifications, the need arises for common definitions, common terminology, common abbreviations and data elements. This cannot be achieved if these elements are spread across different specifications. The SX001G glossary will provide a common reference across all S-series specifications.
Back to the Radar
Click the icon below
to view the details.

## Slide 38: SX002D - Common data model for the S-Series ILS Specifications
Last revised: 2015-02-10
Abstract
With the drive for an integrated set of Integrated Logistic Support (ILS) specifications, the need arises for interoperability between the different data models of the different specifications. This cannot be achieved unless a common core is hared across all specifications
The SX002D defines a Common Data Model across all S-Series ILS specifications, and will cover all elements shared by at least two specifications.
SX002D is based on AP239 and will therefore allow the integration with other domains, such as requirements (AP233) or engineering (AP242) as soon as the different APs have been all integrated.
Back to the Radar
Click the icon below
to view the details.

## Slide 39: SAML - Security Assertion Markup Language
Last revised: 2010-03-11
Abstract
SAML Defines a protocol to exchange, identification and authentication information in order to enable security and confidence through Internet collaboration.
SAML provides distributed SSO functions on the Internet , allowing people to be identify in their own user management system and access distant resources (applications and data) using a unique and proven identity.
Back to the Radar
Click the icon below
to view the details.

## Slide 40: SCORM - Sharable Content Object Reference Model 2004
Last revised: 2012-10-05
Abstract
SCORM describes a technical framework that references a harmonized set of e-learning-based guidelines, specifications and standards. Internationally proven as a training technology, implementations have succeeded through use of a content model to ensure consistent run-time environment behaviours that manage and track distributed learning events across e-learning communities.
SCORM is built upon the work of the Aviation Industry Computer-Based Training (CBT) Committee (AICC), the IMS Global Learning Consortium, Inc., the Institute of Electrical and Electronics Engineers (IEEE), the Alliance for Remote Instructional Authoring and Distribution Networks for Europe (ARIADNE) and others.
It creates one unified "reference model" of interrelated technical specifications and guidelines that meet United States Department of Defense (DoD) high-level requirements for Web-based learning content and systems. South Korea’s Education Ministry has implemented SCORM across all grade levels to manage after-school tutorial programs. SCORM has proven to support a diversity of content and communities.
Back to the Radar
Click the icon below
to view the details.

## Slide 41: SPEC2000 – ATA E-Business Specification for Materiels Management
Last revised: 2018-11-12
Abstract
ATA Spec 2000 is a global aviation specification to automate the business processes and information exchange associated with aircraft parts, materiel, maintenance and reliability. This specification encompasses a wide variety of information exchange and is used broadly by the world's airlines and suppliers.
Spec 2000 was up to 2016 structured into major chapters, each designed to stand alone for ease of understanding, as well as ease of implementation. Appendices are assigned to those subjects common to each chapter.
  Chapter 1 - Provisioning
  Chapter 2 - Procurement Planning - Download Free
  Chapter 3 - Order Administration
  Chapter 4 - Customer Invoicing
  Chapter 5 - Information and Data Exchange
  Chapter 6 - Communications Commands
  Chapter 7 - Repair Order Administration
  Chapter 8 - Repair/Overhaul Planning
  Chapter 9 - Automated Identification and Data Capture - Purchase Separately
  Chapter 10 - SPEC2000/ASC X12 Implementation Guide
  Chapter 11 - Reliability Data Collection/Exchange - Purchase Separately
  Chapter 12 - Airline Inventory Redistribution System (AIRS) - Download Free
  Chapter 13 - Industry Performance Metrics
  Chapter 14 - Warranty
  Chapter 15 - Delivery Configuration Data
  Chapter 16 - Electronic Parts Certification Forms - Download Free
  Chapter 17 - Electronic Logbook
Back to the Radar
Click the icon below
to view the details.

## Slide 42: SPEC2300 - Data Exchange Standard For Flight Operations
Last revised: 2018-11-12
Abstract
The purpose of this specification is to provide a concise set of information standards and guidelines for the management, configuration and interchange of flight operations technical content for fixed-wing and rotorcraft. This Specification is focused on a data-centric approach, addressing the aircraft operator’s current and planned future operational / business requirements of these data. A corner stone of this specification is that these data are stored once, reusable without rework, and the interchange.
This specification is designed to enable the cost-effective and efficient exchange of digital data between information providers and information users for Flight Operations. The primary goals, features, and objectives are:
  Exchange of information based on non-proprietary standards.
  A standard architecture that is data-centric as opposed to document-centric, and relies on modular, reusable components.
  Information from multiple manufacturers is received by operators in a single, consistent manner.
  Facilitate identification of changes to the data.
  Facilitate modification or re-authoring of information.
  Separate presentation of information from the content of the information, enabling output to multiple formats.
  Enable identification of information based on its applicability to specific aircraft or fleets.
  Facilitate re-use of content for different audiences, e.g., Crew Use During Flight, In-House Training, Engineering, Computer-Based Training (CBT).
Back to the Radar
Click the icon below
to view the details.

## Slide 43: STE100 - ASD Simplified Technical English - International specification for the preparation of technical documentation in a controlled language
Last revised: 2017-02-01
Abstract
ASD-STE100 (European Community Trade Mark No. 004901195) is an international specification for the preparation of maintenance documentation in a controlled language. A controlled language is a form of language with special restrictions on grammar, style and vocabulary usage.
It was developed in the early Eighties (as AECMA Simplified English) to help the users of English-language documentation to understand what they read. The ASD-STE100 provides a set of Writing Rules and a Dictionary of controlled vocabulary.
The Writing Rules cover aspects of grammar and style; the Dictionary specifies the general words that can be used. These words were chosen for their simplicity and ease of recognition. In general, there is only one word for one meaning, and one part of speech for one word. In addition to the specified general vocabulary, ASD-STE100 accepts the use of company-specific or project-oriented technical words, provided that they fit into one of the categories listed in the Specification. Control of any additional specific vocabulary is, of course, the responsibility of the company or the project itself.
Back to the Radar
Click the icon below
to view the details.

## Slide 44: STEP - Standard for the Exchange of Product model data
Abstract
STEP provides a comprehensive set of internationally-agreed integrated information models to address the problem of exchanging, sharing and archiving product information across dissimilar computer applications throughout the lifecycle of the product.
Deployment of the STEP standard enables companies to have a proven single definition for all the product-related information related to individual products throughout their lifecycle, independent of changes in process and information technology. The standard will enable suppliers to deliver and receive support information in a consistent form, irrespective of the source. Interoperability is facilitated by the adoption of common subsets of the standard, known as Application Protocols to support particular information flows.
Last revised: 2014-10-23
Back to the Radar
Click the icon below
to view the details.

## Slide 45: STEP AP203 - Configuration controlled 3D design of mechanical parts and assemblies
Abstract
ISO 10303-203:2011 specifies the application protocol for “Configuration control 3D design” edition 2.
The following are within the scope of ISO10303-203:2011:
  Products that are mechanical parts and assemblies;
  Product definition data and configuration control data pertaining to the design phase of a product's development;
  Representation of an instance of a part in an assembly through its usage in a sub-assembly;
  Three dimensional shape representations of a part
  Geometric validation properties to allow the translation of geometric shape representations (advanced boundary representation and faceted boundary representation solids) to be checked for quality;
  Geometric and dimensional tolerances applied to geometric shape representations;
  Materials and their composition of chemical substance;
  Composite material structure and shape;
  Catalogue data characterized by property value pairs;
  Three dimensional presentation of product data:
  Technical drawings as two dimensional presentation of product data.
The first edition has been published by ISO in 1994 and the second edition has been published by ISO in 2011, in a modular form.
Last revised: 2013-04-05
Back to the Radar
Click the icon below
to view the details.
Notes: 45

## Slide 46: STEP AP209 - Multidisciplinary analysis and design
Abstract
In the context of Design/Analysis integration, STEP AP209 is a standard for exchange and long term archiving of information between iterative design and analysis stages of the product life cycle.
First edition of STEP AP209 was published in 2001 under the name “Composite and Metallic Structural Analysis”.
The primary intent of the standard is to combine CAD, CAE and PDM capabilities to enable sharing of PDM controlled composite and metallic design, analysis, and material properties information.
Augmenting shared information between design and analysis, both disciplines have separate but related product definitions allowing support of independent configuration control between the disciplines. Transfer between CAD 3D shape and CAE analysis information may be bi-directional enabling the feedback of information in the iterative design/analysis environment.
A second edition of STEP AP209, renamed “Multidisciplinary analysis and design” is in final stage of development with the DIS submitted end of June 2013.
On top of its migration to the modular architecture, STEP AP209 ED2 has enlarged its coverage beyond the STEP AP209 ED1 classical Finite Element Analysis capabilities:
  CFD, mainly based upon the CGNS standard;
  Generalized structured and unstructured analysis and mesh capabilities, developed under the European Union GEM program;
  Complete discrete/continuous mathematical field representation capability, based upon the David Taylor Labs/Boeing DT-NURBS package.
The result is that STEP AP209 ED2 will now address a much wider set of multi-disciplinary analysis and optimization problems.
Last revised: 2015-02-10
Back to the Radar
Click the icon below
to view the details.
Notes: 46

## Slide 47: STEP AP210 Electronic Assembly Interconnect and Packaging Design
Abstract
In 2001, ISO published the first edition of a STEP Application Protocol for Electronic Assembly Interconnect and Packaging Design (AP 210) as an International Standard. This Application Protocol (AP) provides the groundwork for significant advances in product data reuse and cycle time reduction by defining a standardized, computer-interpretable method for representing the design of:
  Assemblies with electrical content at multiple levels of product hierarchy,
  Assemblies being designed jointly by electrical and mechanical departments,
  Interconnect designed using layered abstraction, typically Printed Circuit Boards (PCBs).
This AP achieves a significant breakthrough in re-usable component models, allowing component suppliers to provide 3D product models with electrical intelligence integrated with catalog data in a computer-interpretable neutral form for the first time.
This achievement was reached through a coordinated effort involving numerous Fortune 500 companies and government organizations including Rockwell Collins Inc., Boeing, Delphi-Delco Electronic Systems, IBM, the US Naval Supply Systems Command RAMP Program Office, and NIST.
A second edition of AP 210 based on STEP modules consistent with APs such as AP 203, AP 209, AP 233 and AP 239 is scheduled for publication in 2010.
Last revised: 2011-01-11
Back to the Radar
Click the icon below
to view the details.
Notes: 47

## Slide 48: STEP AP212 - Electrotechnical design and installation
Abstract
AP 212 is an international standard that specifies data representation for the exchange and sharing of electromechanical plants and industrial systems design information. It addresses electrical product definition necessary to support electrical cable tray: current analysis, equipment, lighting, cable sizing, electrical connectivity checks and cable tray interference detection. This application protocol does not impose any restriction on the usage of these systems for particular applications - equipment for power-transmission, distribution, and generation, electrical machinery, electric light, electric heat, control and automation systems are all in scope.
It was an initiative of the electrical industry and has being developed in cooperation with ProSTEP GmbH, with the help of the German Electrotechnical Committee (DKE) and with the cooperation of other industrial consortia, e.g. GOSET(F) and PDES Inc. (USA), and is standardized internationally as a joint effort of IEC/TC3 and ISO/TC 184/SC 4.
The first edition has been published in 2001 by ISO and since then no further updates or preparation for a new edition have been requested by industry.
Last revised: 2011-01-11
Back to the Radar
Click the icon below
to view the details.
Notes: 48

## Slide 49: STEP AP214 Core data for automotive mechanical design processes
Abstract
This application protocol is one of the relevant STEP APs available for ASD deployment (c.f. STEP blip for more information on this set of standards).
STEP AP214 provides an integrated information models to address the problem of exchanging, sharing and archiving product information related to mechanical design process across dissimilar computer applications throughout the lifecycle of the product, including Product Data Management systems and Computer Aided Design tools dealing with different kind of geometrical representations and metadata allowing to describe product structure, document structure, configuration management information, change process information, effectivity information, person and organization, etc.
Deployment of the STEP AP214 standard enables companies to have a proven single definition for all the product-related information used for mechanical design process, with different views on lifecycle phases considered by the designers.
Last revised: 2013-04-05
Back to the Radar
Click the icon below
to view the details.
Notes: 49

## Slide 50: STEP AP233 - Systems Engineering
Abstract
This application protocol is one of the relevant STEP APs available for ASD deployment (c.f. STEP blip for more information on this set of standards).
STEP AP233 provides an integrated information models to address the problem of exchanging, sharing and archiving product information related to system engineering design process across dissimilar computer applications throughout the lifecycle of the product, including Product Data Management systems and Computer Aided Design tools dealing with different kind of system representations and metadata allowing to describe system structures, document structure, configuration management information, change process information, effectivity information, person and organization, etc.
Deployment of the STEP AP233 standard enables companies to have a proven single definition for all the product-related information used for mechanical design process, with different views on lifecycle phases considered by the system designers.
Last revised: 2010-04-02
Back to the Radar
Click the icon below
to view the details.
Notes: 50

## Slide 51: STEP AP235 Engineering properties for product design and verification
Abstract
STEP AP 235 defines the context, scope, and information requirements for properties of products that can be used for product design and design validation, the testing, measurement and approval processes used to determine those properties and specifies the integrated resources necessary to satisfy these requirements.
Considering that the value of an engineering property of a product is dependent on the process used to measure the property value and on the conditions used in that process, AP 235 provides the means to associate a property value explicitly to the conditions in which it was measured, and thus provide an audit trail to the origins of data values that can be used in product design.
AP 235 enables to represent the relationships between the test piece, the sample and the original product, as the measurement procedure generally requires a representative test piece with specific shape and dimensions.
AP 235 handles the method used to process the engineering properties from the testing results (e.g. central value and associated uncertainty).
Last revised: 2016-09-06
Back to the Radar
Click the icon below
to view the details.
Notes: 51

## Slide 52: STEP AP239 - Product Life Cycle Support (PLCS), Edition 2
Abstract
PLCS provides an internationally-agreed information model to address the problem of keeping the full set of information related to a product in alignment with that product throughout its lifecycle. The required information includes product data management, task descriptions, operating states, planned and unplanned maintenance and complete historical records
Deployment of the PLCS standard will enable companies to have a single definition for all the product-related information related to individual products throughout their lifecycle, independent of changes in process and information technology. The standard will enable suppliers to deliver and receive support information in a consistent form, irrespective of the source. Interoperability will be facilitated by the adoption of common subsets of the standard, known as Data Exchange Sets (DEXs) to support particular logistics information flows, and the use of common reference data libraries to configure the standard for operational use.
Last revised: 2016-09-06
Back to the Radar
Click the icon below
to view the details.

## Slide 53: STEP AP239 - Product Life Cycle Support (PLCS), Edition 3
Abstract
In 2015, a divergence risk was identified between the different versions of STEP PLCS (ISO AP239 ed1, ed2 and the corresponding OASIS PSM specification) and product support standards (AIA-ASD S-Series suite of ILS specifications, SAE). To solve this issue, a PLCS Edition 3 project was proposed to ISO end of 2015.
Objective of this PLCS Edition 3 are to:
  Harness current product life cycle standardization efforts, such as ISO 10303-239 ed 1, ed 2, ASD/AIA S-Series, and SAE GEIA-STD-0007 as inputs in developing baseline requirements for ISO 10303-AP239 ed3.
  Ensure interoperability with AP242 and other STEP APs through the new STEP architecture.
  Incorporate requirements from implementation experience and the Product Support standards.
The project has started in 2016, with the objective to deliver a Draft International Standard in 2018.
Last revised: 2016-09-06
Back to the Radar
Click the icon below
to view the details.

## Slide 54: STEP AP242 Managed Model Based 3D Engineering, Edition 1
Abstract
For 20 years a significant amount of effort has been made by the Aerospace and Automotive industry to develop two parallel STEP standards: AP 203 edition 1 was published in 1994, primarily driven by Aerospace and Defence requirements and developed and maintained by PDES, Inc. AP 214 edition 1 was published in 2001, driven primarily by automotive requirements, and developed and maintained by the ProSTEP iViP and SASIG organizations.
The ASD SSG working jointly with ProSTEP iViP, and NIST working jointly with PDES, Inc. have identified an opportunity for a convergent AP, based on AP 214 edition 3 and AP 203 edition 2. As a response, a new project has been launched by ISO TC 184/SC 4: ISO 10303-242 in 2010.
The main technical requirement for AP 242 ed1 is to become the cornerstone standard of the cross-process capabilities for interoperability of core engineering design information under configuration management, that is to say,
  Providing specifications for exchange and long term archiving,
  Providing a consistent business object model used for XML exchange and PLM web services, and
  Providing a data model for 3D tessellated model
Last revised: 2015-02-10
Back to the Radar
Click the icon below
to view the details.

## Slide 55: STEP AP242 Managed Model Based 3D Engineering, Edition 2
Abstract
STEP AP 242 edition 1 standard is the result of the convergence of STEP AP 203 ED3 and AP 242 ED3; this standard is described by a specific component summary: Application Protocol 242 “Managed Model Based 3D Engineering” edition 1.
The industry has launched a project to increase the functionalities of the edition 1 to several domains. The goal is to consolidate the key role of STEP AP 242 as the backbone information model for Core 3D design information, covering progressively the different technical disciplines requested by the manufacturing industries.
The main extensions of AP 242 edition 2 are for Electrical harness for design and construction, and for 3D additive manufacturing / 3D printing design information.
Last revised: 2014-10-22
Back to the Radar
Click the icon below
to view the details.

## Slide 56: SysML - Systems Modeling Language
Abstract
SysML is a standardized modelling language defined by International System Engineering community dealing with complex systems of systems, with a strong involvement of Aerospace&Defence industry.
The focus is to support Computer Aided modelling of systems for requirements, analysis, design, verification and validation purpose, being specific system modelling applications independent (organization or used software product).
This standard does not address only data interchange of data between applications, but also standardized visual modelling language dedicated to people producing system informational and behavioural models. It is achieve by defining it as a dialect (profile) of the second version of the Unified Modelling Language (UML2).
This language can consequently be used for interchanging models between people, system modelling/simulation platform and information/models management systems.
As all simulation and system modelling tools are not necessarily based on SysML, and as UML model interchange format (XMI) is still not very mature, SysML is also aligned with ISO STEP application protocol dealing with System Engineering (AP233), allowing interchange and long term archiving of data representing systems all along the phases of the lifecycle of complex systems of systems within Aerospace and Defence industry.
Last revised: 2010-04-02
Back to the Radar
Click the icon below
to view the details.
Notes: 56

## Slide 57: TDP Message - Technical Data Package Message
Abstract
The aim of the Technical Data Package Message project is to standardize the TDP message that will be used for TDP exchange processes and services related to online transportation of TDP, secured transfer, monitoring, history and acknowledgment procedure for product data import and export.
Based on the more relevant existing PLM eBusiness standards and associated frameworks, the TDP message should be useable with legacy exchange protocols, standardized or not, and useable for any kind of exchange all along the phases of the lifecycle of a product. TDP transportation and TDP data exchange are fully decoupled. For this reason, TDP message and Product metadata are considered separately. It allows addressing very simply the transportation, being independent of the application protocol used for Product Meta Data.
The product data exchange, related to product data import and export between PDM solutions and CAD/CAM/CAS tools is out of scope.
Last revised:2012-10-05
Back to the Radar
Click the icon below
to view the details.
Notes: 57

## Slide 58: TSCP SEv1 - Secure Email v1
Abstract
The Transglobal Secure Collaboration Program (TSCP) is a government-industry partnership specifically focused on mitigating the risks related to compliance, complexity, cost and IT that are inherent in large-scale, collaborative aerospace and defense programs that span national jurisdictions.
The TSCP Secure E-mail v1 specification allows organizations to send digitally signed and/or encrypted email. About 49.6 billion e-mail messages (spam excluded) are sent every day worldwide. E-mail has become an indispensable part of the business fabric of every enterprise.
Much of e-mail traffic generated by aerospace and defense companies and government organizations is sensitive and must be protected against eavesdropping. In addition, due to inherent security weaknesses in the Simple Mail Transfer Protocol (SMTP), the e-mail protocol of the Internet, it is easy to forge and modify messages. Attackers can make e-mail messages appear as coming from legitimate users or modify their content to suit their purposes. The TSCP Secure E-Mail Specification is proposed to address these concerns.
The TSCP Secure E-Mail Specification v1 will be more widely implemented and used to provide confidentiality and integrity for e-Mail exchanges, if the specifications and key supporting documentation are made publicly available and their usage is encouraged by adoption as industry specifications in Europe and the US.
Last revised: 2011-11-17
Back to the Radar
Click the icon below
to view the details.
Notes: 58

## Slide 59: UAF – OMG Unified Architecture Framework
Abstract
The Unified Architecture Framework (UAF) is a generic architecture framework building on UPDM (the Unified Profile for DoDAF and MODAF) and on existing architecture frameworks, including DoDAF (DoD Architecture Framework), MODAF (UK Ministry of Defence Architecture Framework) and NAF (NATO Architecture Framework).
UAF is aligned with ISO 42010 (Architecture Description) and includes three components:
  Predefined viewpoints and levels of abstraction, organized in a grid:
    Domains: Metadata, Strategic, Operational, Services, etc.
    Model kinds: Taxonomy, Structure, Connectivity, Processes, etc.
  The UAF Domain Meta-Model (UAF DMM) is an open and non-implementation specific meta-model (e.g. non-UML tool vendors can implement it). The UAF DDM is structured on the above grid and provides a basis for semantic interoperability between architecture stakeholders and developers.
  The UAF Profile (UAFP), a standard UML profile that can be used to implement the UAF in a UML (or SysML) tool.
Last revised: 2018-11-12
Back to the Radar
Click the icon below
to view the details.
Notes: 59

## Slide 60: VDA 4968 VEC KBL “Kabelbaumliste” - Harness Description List
Abstract
During the last years, the target of the VDA Working Group “Car Electric” (with participation of major OEMs and harness suppliers) is the improvement of the development process of vehicle electrical system and its integration into the entire vehicle development process. Therefore the concept of vehicle electric container, which contains all required parts of the electrical system, was developed, based on ISO 10303-212 “Electrical Design and Installation” standard.
The Vehicle Electric Container (VEC) has four different parts:
  The Harness Description List (KBL; stands for "Kabelbaumliste”)
  The Electrical Logic (ELOG)
  The Component Model (KOMP) and
  The Geometry Model (GEO).
The harness description list, which is described in the VDA recommendation 4964, was the origin and later extended by the other parts to the vehicle electric container.
The KBL part contains:
  Harness, variants and modules
  Components
  Parts lists
  Connectivity lists
  Topology
It is based on the STEP standard AP 212.
Last revised: 2010-06-23
Back to the Radar
Click the icon below
to view the details.
Notes: 60

## Slide 61: VDA 4969 - Simulation Data Management in Integrated Collaborative CAD/CAE Process Chains
Abstract
The C³I recommendation (VDA 4969), published by the German Association of the Automotive Industry (VDA) and the ProSTEP iViP Association, provides an open and commonly available description of requirements, processes and use cases for the cross-enterprise and cross-domain integration of simulation and computation. It builds on the “Integration of Simulation and Computation in a PDM Environment (SimPDM)” recommendation (VDA 4967).
It defines processes, relations and use cases which fulfil the requirements regarding communication and integration. This covers cross-enterprise and cross-domain scenarios as well as the interaction between authoring tools and data management systems. The recommendation also gives standardized definitions of CAE process modules and simulation data management (SDM) core functionalities.
In order to enable system support, the recommendation also defines a general metadata model and describes possible system extensions. The C3I metadata model is designed in a modular way to allow custom tailoring of solutions, and a mapping to existing data formats is given to illustrate how established interfaces can be extended to fulfil the requirements described in this recommendation.
The recommendation does not define an interchange format between different CAE applications.
Last revised: 2014-08-25
Back to the Radar
Click the icon below
to view the details.
Notes: 61

## Slide 62: XPDL - XML Process Description Language
Abstract
The XML Process Description Language is the format for storing and interchange workflow models that can be executed by Workflow systems as specified by Workflow Management Coalition. It is aligned with the Object Management Group’s Business Process Modelling Notation (c.f. BPMN Blip), which is a visual process notation standard endorsed by Wfmc, and broadly adopted across the industry.
Knowing that numerous Product Data Management Systems include a workflow execution component, which allows controlling data through change management process, XPDL is a mean to interchange PLM workflow process models between PDM systems.
Last revised: 2011-11-14
Back to the Radar
Click the icon below
to view the details.
Notes: 62

## Slide 63: No blip description available
Sorry!
ASD SSG plans to provide a description for this component standard in one of the next Radar Chart versions.
Back to the Radar
Notes: 63